## Slide 1: Software Engineering and Architecture
Energy Efficiency
An important Quality Attribute

## Slide 2: Motivation
Well… Large and important topic !
I will delimit myself to energy-efficiency
… or
Ala: Patient Inger’s blood-pressure is uploaded to server
  Architecture A spends 3.1mJ; Architecture B spends 6.7mJ
  We prefer architecture A, right?
Notes: Source: https://www.ibm.com/cloud/blog/green-computing

## Slide 3: Energy and Power
We are basically interested in energy
  Energy = Amount of work
Energy is measured in Joule (SI unit)
    1J work is done when a force of 1 newton displaces a mass 1 meter
      Newton = force accelerating 1kg by 1m/s^2
Power is measured in Watt
  Power = energy / second; 1 W = 1 J/s
    Or…
  1 Joule is 1 W in 1 second = 1 Ws
  1 KWh = 3.6 MJ
100g Hellmann’s Mayonnaise contains 2,965,000 J (0.82 kWh) About 35 min sweaty bicycling…

## Slide 4: Motivating Example
Gangnam Style
  Was shown 1.7 x 10^9 times the first year
  Energy to stream once is 0.19kWh
  Total: 312 GWh
  Danish average house (“parcelhus”) yearly electricity consumption
    4.4 – 5.0 MWh
  ~ 70.000 Danish houses
Morale: None… But it is a bit thought provoking…
Notes: Source: https://www.sciencedirect.com/science/article/abs/pii/S0164121216000777;
https://www.ok.dk/privat/hjaelp/el/elforbrug/hvad-er-et-typisk-aarsforbrug-af-el

## Slide 5: Energy = Work Done
Hardware spends energy, because our Software wants work to be done.

## Slide 6: Koomey’s Law
Hardware consumes energy
  But is improving all the time!
    They are the good guys!
  The curve is flattening though…
Notes: https://en.wikipedia.org/wiki/Koomey%27s_law

## Slide 7: Wirth’s Law
Unfortunately, we as developers and architects are terrible at writing software or writing too much 
  We are the bad guys!
Example:
  A ‘small’ linux desktop: Lubuntu
  First used in 2016, easily ran in a 2GB RAM VM 
  Last 24.04 version, has issues running in a 4GB RAM VM 
  No real perceived benefits! But 3.4 times larger…
Notes: https://en.wikipedia.org/wiki/Wirth's_law

## Slide 8: What is Power used for?
Note
  CPU drives much else
    Heat/fan to cool when high load
  Note
    SSD+DRAM is ‘cheap’ power wise…
275W
15W (~5%)
Out-of-box: Network. Devices: Display, Sensors (GPS, accelerometer, sound, …)
Notes: Kempen et al (2024) finds 2-8% of energy is by RAM.
https://computerinfobits.com/how-much-energy-do-gaming-computers-use/
Other source:
https://www.buildcomputers.net/pc-power-requirements.html.

## Slide 9: What is Power used for?
Note
  CPU drives much else
    Heat/fan to cool when high load
  Note
    SSD+DRAM is ‘cheap’ power wise…
275W
15W (~5%)
Out-of-box: Network. Devices: Display, Sensors (GPS, accelerometer, sound, …)
The Apollo 13 Team returned safely to earth, but was heavily water rationed during their perilous return flight – because they needed the water to cool the guidance computer!
Notes: Kempen et al (2024) finds 2-8% of energy is by RAM.
https://computerinfobits.com/how-much-energy-do-gaming-computers-use/
Other source:
https://www.buildcomputers.net/pc-power-requirements.html.

## Slide 10: Examples: My Starting Lab
The Lab
  Fujitsu Esprimo Q900 (2012)
  MSI Trident (2020)
Installed with Ubuntu 22.04 LTS
  Headless
    No use for the GeForce RTX™ 2080 Ti 
Idle Power Consumption
  Esprimo: ~ 11 W (plug) / 2.8 W (CPU)
  MSI: ~ 40 W (plug) / 7.4 W (CPU)
    At ~95% CPU load@Plug: Esprimo 43W and MSI 160W
Notes: Full throttle: Esprimo ~43W, MSI ~160-120W

## Slide 11: For Workshops
For teaching
Still rather Storm P like 

## Slide 12: The Framework
The Green Architecture framework 
https://baerbak.cs.au.dk/papers/gaf.html

## Slide 13: Processes
How we design Green Architectures?

## Slide 14: Measure and Experiment
You need to measure!
You need to experiment!

## Slide 15: Measurements
Options
  Measure wall power
    Get going for ~100kr
  Measure on-chip power
    RAPL: Running Average Power Limit
    powerstat (linux)
    power gadget (windows)

## Slide 16: Be Systematic
As in Physics
  Control the environment, reduce error sources
  Make many experiments, large sample size
  Use proper statistical methods
Luiz Cruz (2021)
  https://luiscruz.github.io/2021/10/10/scientific-guide.html

## Slide 17: Prioritize Effort
Prioritize Effort
  Know the usage profile
    (by measurements )
  And invest your effort where it counts
    Those user stories that are executed the most and that can be optimized the most – are the ones to spend your effort on optimizing
      Sounds reasonable, but you need to know the usage profile 

## Slide 18: Increase Awareness
Increase Awareness
  All architects/developers/ stakeholders informed about how to increase energy-efficiency
From my kitchen. Which one is 2W and which 40W?
  You have to tell the kids which one to prefer 

## Slide 19: Tactics
How do we then do Green Architecting?

## Slide 20
Set of tactics
  Architectural design decision to impact energy-efficiency
Quite a lot of tactics under seven main categories
  Some of which are a bit “above your current pay-grade” 
SWEA picks follows…

## Slide 21: Bulk Fetch Data
“Buy 50 things at the super market once, instead of making 50 trips buying a single thing”
  POSA4(2007): Batch Method
    Iterator pattern is an energy anti pattern
      getNext() across the network is a chatty interface
      Use pagination instead – bulk fetch next 50 items in one chunk
Notes: Source: Patterns of Software Architecture Vol 4 / Buschmann et al.

## Slide 22: Bulk Fetch Data
“Buy 50 things at the super market once, instead of making 50 trips buying a single thing”
Example
  Classic OO is often a very fine-grained API
The UI needs to get all card data from the server when redrawing UI…
Notes: Source: Patterns of Software Architecture Vol 4 / Buschmann et al.

## Slide 23: Example of A/B Architecture
The Card interface
  Two remote implementations
Broker pattern Classic (RMI-like)
Broker pattern Batch Method
a) Cache 5 secs b) Get PODO

## Slide 24: Bulk Fetch Data
“Buy 50 things at the super market once, instead of making 50 trips buying a single thing”
Comparison
  Classic Broker (the one you make)
    5.66W (σ 0.90W)
  Batch Method Broker (using caching)
    4.12W (σ 0.79W)
    (Reducing number of network calls to 43%)
  Saving 27% energy
    And this is on the server side only!
Notes: Source: Patterns of Software Architecture Vol 4 / Buschmann et al.

## Slide 25: Fetch Data from the Proximity
“Have a stock of supplies to avoid a lot of trips to the super market”
Cache Data Closer to User
  The Batch Method Broker is one such example
  Content-Delivery-Networks (CDN)
    Store web contents (caching) physically near to the users to provide faster load times by avoiding “long distance network transmission”

## Slide 26: Utilize an Efficient Technology
“Switch the 20 W halogen bulb to a 4 W LED bulb”
Use Efficient Languages and Tools
  (This 2017 study used rather unrealistic benchmark programs)
    Mandelbrot???
Own experiment of a 3 endpoint REST Service impl:
Java (baseline) Go (-3.5% energy)
Scala (+27% energy)
Python (+162%, 2½x)
Notes: Source: https://greenlab.di.uminho.pt/wp-content/uploads/2017/10/sleFinal.pdf
C is the baseline language (=1) in energy consumption.

## Slide 27: [SideBar]
Statistics is rather essential here
  Thanks to Markus from Statistics and all his predecessors 
Question
  Is Go really 3.5% more efficient or is it due to statistical uncertainty?
Answer
Do a Welch T-test
  Using Gnumeric
  p-value < 5% 
Own experiment of a 3 endpoint REST Service impl:
Java (baseline) Go (-3.5% energy)
Scala (+27% energy)
Python (+162%, 2½x)

## Slide 28: Utilize an Efficient Technology
“Switch the 20 W halogen bulb to a 4 W LED bulb”
Use Low-footprint Data Formats
    XML is much more verbose than JSON
    Binary formats: ProtoBuf, Cap’n Proto
  Part-time students did a XML versus JSON experiment
JSON: 24.5W (σ 2.5w)
XML: 27.9W (σ 4.1W)
That is 12.2% saved energy by using JSON over XML
Notes: Meta: Group Delta/F2023/Mandatory 6. TeleMed storage load scenario.

## Slide 29: Utilize an Efficient Technology
“Switch the 20 W halogen bulb to a 4 W LED bulb”
Use Efficient Databases
    If only a ‘blob storage’ / key-value store is necessary then pick one, rather than a SQL or a MongoDB database
  Example
    REST service (three endpoints: One POST and two GET)

## Slide 30: Utilize your Resources Efficiently
“Prepare several items in the oven at the same time”
An idling computer spends between 1/4 - 2/3 power compared to a busy computer
    The non-proportionality of energy consumption
Which means:
  Per-transaction energy cost is lowering as the computer is more heavily utilized

## Slide 31: Utilize your Resources Efficiently
“Prepare several items in the oven at the same time”
Imagine a single server
  Handling 2.000 tps at 100% CPU load
    Result: 2.000 tps spending 90 W
Chart: Primenergy TX100 (Xeon E3-1200 4 core)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 75 | 80 | 90 | 95 | 98
RAPL | 5.24 | 6.09 | 6.89 | 8.11 | 10.94 | 17.12 | 19.52 | 21.96 | 23.17 | 24.62 | 27.12 | 28.14 | 28.57
59,0 | 59 | 58 | 60 | 64 | 72 | 75 | 78 | 81 | 83 | 86 | 87 | 87
90W

## Slide 32: Utilize your Resources Efficiently
“Prepare several items in the oven at the same time”
Change to Horizontal Scaling: Two servers
  Handling 1.000 tps each at 50% CPU load
    Result: 2.000 tps spending 2 x 75 W = 150 W
Chart: Primenergy TX100 (Xeon E3-1200 4 core)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 75 | 80 | 90 | 95 | 98
RAPL | 5.24 | 6.09 | 6.89 | 8.11 | 10.94 | 17.12 | 19.52 | 21.96 | 23.17 | 24.62 | 27.12 | 28.14 | 28.57
59,0 | 59 | 58 | 60 | 64 | 72 | 75 | 78 | 81 | 83 | 86 | 87 | 87
Morale: Make your CPU do as much work as possible!
90 W versus 150 W
75W
And a surplus energy consumption by the load balancer…
1.6x energy!

## Slide 33: Utilize your Resources Efficiently
“Prepare several items in the oven at the same time”
Pool Physical Machines (Cloud)
    Host a lot of VM on same physical machine means when A is not using the CPU, then B have it
      Cloud centers are better at that than on-premise
Pool Resources (Threads/Connections)
  Threads and connections are expensive to create and deallocate
    Pool them
Own experiment: Three-tier system with MariaDB storage. A) Naïve ‘connection-pr-request’ connector; B) C3P0 ‘pool’. Pooled connection spent about 62.5% less energy.
Naïve: 192tps C3P0: 514 tps
Disclaimer: Naïve had coarse-grained locks applied…
Notes: Re the note: The Naïve variant could not cope with the load, and threw SQLExceptions, which lead to the conclusion of race conditions. I put ‘synchronized’ on all connector methods, which is rather brute force. It worked, but the TPS is probably lower than could be achieved by a more detailed study…

## Slide 34: Accept Lower Fidelity
“Turn the room temperature down from 21° to 19°”
Replace Dynamic Contents with Batch
    Change webpage dynamic content (expensive) with batch once-per-hour (or per-day) computation of a static webpage (cheap)
Lower Fidelity of Video/Images
    Use 720p instead of 1080p (halves the size)
    Downscale images server side
      Use JPEG rather than GIF/PNG

## Slide 35: Accept Lower Fidelity
“Turn the room temperature down from 21° to 19°”
Avoid Feature Creep
  Do we really need it all???
Maybe it is about time, we start taking out features, instead of just adding more!
Light editions with Green Label.
Notes: WarStory: Kommunal IT indkøbschef i khb området: Vi har lige købt system X udelukkende fordi det kunne mere end konkurrenterne!

## Slide 36: Accept Lower Fidelity
Avoid Feature Creep
‘PizzaLand’ Experiment: A ‘core’ REST based pizza ordering system with ordering and inventory system in MariaDB; deployed on a 2012 i5 CPU @ 2.5GHz/4 core + 8GB DDR3 RAM
Handles 51,800 orders per hour!

## Slide 37: And another Category…
… which is not really about software…

## Slide 38: Do Not Buy New Stuff
Potential Addition to Green Architecture Framework
  Keep the old machines running
    More of a hardware tactic but…
  Laptop running 8h a day for 4 years
    Daily computations 61.5 kg CO2eq
    Production and Shipping 361 kg CO2eq
  Thus around 75-85% of total emissions is manufacturing!
https://circularcomputing.com/news/carbon-footprint-laptop/
Notes: Embodied emissions (due to hardware production of new computer after you replace the old one): For consumer laptops, embodied emissions make up 75-85% of total emissions, and the general pattern is the same for servers. (https://www.gustavwengel.dk/greener-cloud-computing)

## Slide 39: Summary and Discussion

## Slide 40: Summary
Questionnaire to part-time students

## Slide 41: Summary
However, they all require an investment…
  More complex code
  Experiments are time consuming!
Low Hanging Fruits (?)
    Get utilization of CPUs up to ~75%
    Low-footprint data formats
    Bulk fetch data + Caching
    Keep your old machines running

## Slide 42: Discussion
Many of my colleagues have a rather narrow focus
  They are scientist digging deep into the subject matter
    All fine, but …
    … what about all the other important stuff?